| CRANE LIFT PERMIT |
| --- |
| Date: |  | Job Location: |  |
| Work/Task/Project Description: |  |
| Company: |  |
| Permit Receiver (Name): |  | Signed: |  |
| Receiver Phone No. (Mobile): |  |  |  |
| Permit Issuer (Name): |  | Signed: |  |

| PERMITS OVER 1 DAY (MAX 5 DAYS) |
| --- |
|  | Day 2 | Day 3 | Day 4 | Day 5 |
| Date: | / / | / / | / / | / / |
| Receiver: | Sign Here | Sign Here | Sign Here | Sign Here |
| Issuer: | Sign Here | Sign Here | Sign Here | Sign Here |
| Ensure all newly identified hazards and/or changes are communicated to the entire team |

| Crew | Lifting Gear |
| --- | --- |
| Operator & Rigger hold a current licence & competency | Y / N | Has all the lifting equipment been quarterly tested and tagged, are the tags all in date | Y / N |
| Are the crew experienced in undertaking this task safely | Y / N | Has the lifting equipment been inspected immediately prior to use for defects | Y / N |
| Have the crew established a clear method of comms | Y / N | Have the SWL/WLL of the slings, shackles etc been checked for the load applied | Y / N |
| Have the crew discussed the task and reviewed the lift plan/JSA | Y / N | Have the angles and rigging method been considered in checking the lifting capacity | Y / N |
| Lift | Y / N | If using man cage have all components been checked | Y / N |
| Has the area of the lifting operation been protected using barricades and/or spotters | Y / N | Load |
| Any chance of the load impacting the boom or crane body | Y / N | Is the weight of the load and rigging, fly, hooks etc known to all persons involved in the lift | Y / N |
| If the lift involves lifting personal, is the an anti-block device installed and has it been tested immediately prior to the lift | Y / N | Has an appropriate load chart for crane configuration been selected | Y / N |
|  | Y / N | Is the load free of loose unsecured items | Y / N |
| Crane | Environment & Work Area |
| Have the pre/post start operational checks been completed | Y / N | Have the PMNZ Engineers been consulted and notified in writing | Y / N |
| Are all the cranes safety devices functioning | Y / N | Has the PMNZ manager/supervisor for operational area been consulted and notified in writing | Y / N |
| Have the ground/structure conditions been assessed for bearing capacity and determined to be adequate. | Y / N | Is the: wind speed, weather (including lighting) and sufficient light been assessed and deemed within safe limits | Y / N |
| Will the crane be setup with outriggers fully deployed and supported on the correct crane mats | Y / N | Has an inspection of the work area for underground and above ground services been conducted (powerline 10m) | Y / N |
| Is the lift within the specific limits of the specific load charts for the configuration and radius | Y / N | Has consultation been undertaken with all affected parties. | Y / N |
| Other controls: |  |

| Rescue Plan: |  |
| --- | --- |

| WORKERS ON SITE PRINT AND SIGN YOUR NAME IF YOU HAVE READ AND AGREE WITH THE PERMIT CONTENT |
| --- |
| Name | Signature | Name | Signature |